I'm bringing this over here for future reference...



HVAC AGE CODES IN SERIAL # INFO


Amana: BLACKHORSE. B=1971 or 1981. (Of course, now that they've been bought by Goodman, who knows what'll happen.)

BARD 1962 to March 1980
Sample Number 123456 A D

1st six digits are the Unit Identity Number. In this example they are represented by the numbers 123456. 

7th digit is the month of Manufacture. (The letter A in the Sample represents January). 
A = January 
B = February 
C = March 
D = April 
E = May 
F = June 
G = July 
H = August 
Letter “I” was not used. 
J = September 
K = October 
L = November 
M = December 

8th digit is the year of Manufacture. (The letter D in the Sample represents 1964). 
1962 = B 
1963 = C 
1964 = D 
1965 = E 
1966 = F 
1967 = G 
1968 = H 
Letter “I” was not used. 
1969 = J 
1970 = K 
1971 = L 
1972 = M 
1973 = N 
1974 = O 
1975 = P 
Letter “Q” was not used. 
1976 = R 
1977 = S 
1978 = T 
1979 = U 
1980 = V 


Bard April & May 1980

Sample number 123 D A 123456

1st three digits are the Compressor Part Number. 

4th digit is the month of Manufacture. In this sample D represents April. 
D = April 
F = May 

5th digit is the year of Manufacture. In this sample A represents 1980. 
1980 = A 

This serial number style was only used during the months of April & May 1980. 

6th thru 11th digits represent the Unit Identity Number. 


Bard June 1980 to Current

Sample number 123 H80 1234567 02

1st three digits = Compressor Part # 

4th digit = Month 
A = January 
B = February 
C = March 
D = April 
“E” was not used 
F = May 
“G” was not used 
H = June 
“I” was not used 
J = July 
K = August 
L = September 
M = October 
N = November 
“O” was not used 
P = December 

5th & 6th digits = Year 

80 = 1980 
81 = 1981 
82 = 1982 
right on thru. The year 2000 started the numerical numbering from 00. 
00 = 2000 
01 = 2001 
02 = 2002 
right on thru to current date. 

7th thru 13th digits = Unit Identity # 

14th & 15th digits = Factory Code (01=OH; 02=GA)


Carrier, Bryant, Payne, Day & Night: Recently (last 20 years or so) the first four numbers in the serial number represent the week and year. Previously, it was a complex series of letters and single digits. Call 905 672-0860 if you get stuck.

Coleman: Serial numbers prior to April 1992=1st two numbers are month, then year, then series.
After April 1992, 1st two numbers are year, then month, then series.

Comfortmaker (International Comfort) uses the first letter for the month (skipping I) and the first two digits are the year.

First Company Service Parts is one of 4 divisions of First Operations. They supply OEM equipment to all of the major HVAC manufacturers. They are located in Dallas, Tx at 214-388-5751. Harold Hammer at Tech Support (ext#5) will answer your questions.

Goodman: First two digits of the serial number are the year. Second two are the month.
Btu rating is model number..ie; GMP075-3 (75,000 bonnet input)
Compressor is same :serial # 9709088872 (yr1997 wk 09) Tonnage is model # CK361C The first two numbers after the CK (letters) divided by 12 is tons. ie: 36 div by 12= 3 tons.

Lennox: Either the first two or second two digits are the year, it varies by era, but most of them actually have a separate sticker somewhere that has the year printed on it. Newer ones are first two equals manufacturing plant #, 2nd two are year and letter in fifth slot is month (A thru M minus I). So 5898G 07568 would be Plant # 58, Year of MFR would be 98 and month would be July.

Rheem & Rudd: in the middle of the serial number will be a letter "F" the following four numbers are the week and year.
The first letter of the serial number gives the year of manufacture as follows: 

TRANE
Trane uses alpha codes in their serial numbers to determine year of manufacture. They started this in 1987 with the letter B and skipped a couple of letters during the years........ The first letter of the serial number gives the year of manufacture as follows: 

In 2002 they started their serial numbers with the year it was built. In 2002 the first character of the serial number is 2, in 2003, 3 and so on.

Z=2001 
R=2000 
P=1999 
N=1998 
M=97 
L=96 
K=95 
J=94 
H=93 
G=92 
F=91 
E=90 
D=89 
C=88 
B=87 
S=86 
Y=85 
X=84 
W=83 
U=82(seventh digit) 
T=81(seventh digit) 
O, A=80(seventh digit)


YORK (Unitary Products since 1984)
Note: they skip the letters I, O, Q, U, Z.
Year of make indicated by 3rd letter in the serial number.
Fraser, Johnston and Luxaire were purchased by York in 1980.

1971 - A 
1972 - B 
1973 - C 
1974 - D 
1975 - E 
1976 - F 
1977 - G 
1978 - H 
1979 - J 
1980 - K 
1981 - L 
1982 – M 
1983 – N 
1984 – P 
1985 - R
1986 - S
1987 - T
1988 - V
1989 - W
1990 - X
1991 – Y
1992 – A
1993 - B
1994 - C
1995 – D
1996 - E
1997 - F
1998 - G
1999 - H
2000 - J
2001 - K
2002 - L
2003 - M
2004 - N
2005 - P
2006 - R
2007 - S

lkage

1/2/06, 9:25 AM

Thanks, Dave. I was just redoing mine...this is faster.

jwilliams4

1/2/06, 2:45 PM

Good job, Dave.
I thought about doing that, but thinking always gives me a headache.

It's a good thing you're around.

dvalley

1/2/06, 6:49 PM

Bill,

It would be great if you could post your Bradford White (and any other water heater) information that you may have, in the Plumbing forum.

jhanna1

1/2/06, 6:54 PM

Thank's for the info Dave!:D

rray

1/3/06, 6:28 AM

"Technical Reference Guide"
Published by Carson Dunlop Weldon & Associates, Toronto, 2001
ISBN 1-895585-90-2
http://www.carsondunlop.com

This is exactly why we need to sort through the archives, pull out all the reference materials, and publish them somewhere.

http://www.nachi.org/forum/showthread.php?t=95

bsmith

1/3/06, 9:24 AM

Here are a few more--

Weil-McLain

Please look on the outside jacket of the boiler for a CP Serial Number. It will have a bar code on it. Call (or email) Wiel McLain and they will tell you the date of manufacture. Phone: 219-879-6561 ask for Technical Services

Peerless

Prior to 1984 there was not a date code included as part of the serial number. Starting in 1984, there was a four digit date code following the serial number that was month and year. Example – JO-12345-1084, this unit was built in October of 1984. Starting in the year 2000, same idea only it was a six digit date code following the serial number that is year and month. Example – 1234567-200105, this would have been build in May of 2001. Anything without the addition to the serial number would have been made before 1984 and would require contact with the factory.

vBulletin v3.5.2, Copyright ©2000-2006, Jelsoft Enterprises Ltd.

Ducane uses two different formats on serial numbers.  All of our serial numbers are ten characters.  The most common format is all ten characters are numeric.  In this format the last 4 numbers indicate the year and the week of the year.  An example is your serial number 4140720320 where the 03 is 2003 and the 20 is the 20th week of the year (2002).  The more recent format is ten character and the format is the first 4 characters are numeric, the fifth character is alpha, and the last 5 characters are numeric.  The year code is determined from the 3rd and 4th characters that would be the last 2 digits of the calendar year (93=1993 and 06=2006). The fifth character which is alpha represents the month with A=January and M=December and but we do not use the letter I.  This is an example of second serial number format, 4603M12345, the 03 is 2003 and the M is December.

Hope this helps you out.

Ann A Harker 
Allied Air Enterprises 
Consumer Services Specialist 
ann.harker@alliedair.com 
800-515-3501 
FAX 866-412-9014