# Heat Pump Inspection Checklist

## Capacity

- Check to ensure it’s not undersized for heating ____

- Check to ensure it’s not oversized for cooling ____

### Compressor

- Check for excess noise or vibration ____

- Check for short cycling ____

- Check to determine whether it runs continuously ____

- Check to ensure it’s level ____

- Check to ensure it isn’t drawing excess electrical current ____

- Check to ensure the breakers or fuses are correctly sized ____

- Check to ensure that the electrical conductors are properly sized ____

- Check to ensure an electrical shutoff is present and properly sited ____

- Check to determine whether it’s operative in the heating/cooling modes ____

- Check to determine whether it is cooling adequately ____

#### Outdoor Coil

- Check to ensure the coil is clean ____

- Check to ensure the coil is undamaged ____

- Check for excessive corrosion on the coil and components ____

- Check whether the water heater or clothes dryer exhausts are too close ____

- Check whether it’s iced up ____

- Check to ensure that its location is appropriate ____

#### Indoor Coil

- Check whether the temperature split is too high ____

- Check whether the temperature split is too low ____

- Check whether there is adequate access to the coil ____

- Check whether the coil is dirty ____

- Check whether the coil is frosted up ____

- Check to ensure the top of the coil is dry in cooling mode ____

- Check for excessive corrosion ____

- Check for physical damage to the coil ____

#### Condensate System

- Check whether the pan is leaking or overflowing ____

- Check to see whether there is dirt in the pan ____

- Check to see whether the pan is cracked ___

- Check for inappropriate pan slope ____

- Check for a rusted pan with holes in it ____

- Check to ensure the pan is well secured ____

- Check to see whether there is an auxiliary pan ____

- Check for a float switch ____

#### Expansion Device

- Check whether the capillary tube is crimped, disconnected or leaking ____

- Check whether the thermostatic expansion valve is loose, clogged or sticks ____

#### Outdoor Fan

- Check for excessive noise or vibration ____

- Check to ensure the fan is running ____

- Check for excessive corrosion ____

- Check for mechanical damage to the fan ____

- Check for obstructed airflow ____

- Check for a dirty fan ____

#### Indoor Fan

- Check to ensure it isn’t undersized

- Check to ensure any belts or pulleys are properly adjusted ____

- Check for excess noise or vibration ____

- Check for a dirty fan ____

- Check for a dirty or missing filter ____

- Check to ensure the fan is operational ____

- Check for excessive corrosion ____

- Check for mechanical damage to the fan ____

#### Duct System

- Check whether the system is undersized for cooling ____

- Check whether the system is complete ____

- Check to ensure the ducts are clean ____

- Check for disconnected or leaking ducts ____

- Check for obstructed or collapsed ducts ____

- Check for poorly supported ducts ____

- Check for a poorly balanced system ____

- Check to ensure there is a damper in the humidifier ____

- Check to ensure sufficient number of supply/return registers ___

- Check to ensure the supply/return registers are appropriately located ____

- Check to ensure the supply/return registers are not obstructed ____

#### Duct Insulation

- Checking for missing duct insulation ____

- Check for incomplete/damaged duct insulation ____

#### Vapor Barrier

- Check to ensure there is a complete vapor barrier ____

- Check to ensure the vapor barrier is not damaged ____

#### Condensate Drain Line

- Check to ensure the condensate drain isn’t leaking, damaged or split ____

- Check to ensure the condensate drain isn’t disconnected or missing ____

- Check to ensure the condensate drain isn’t blocked or crimped ____

- Check to ensure there is a trap on the condensate drain line ____

- Check to ensure the condensate drain discharges to an appropriate location ____

#### Condensate Pump

- Check to ensure the pump is functional ____

- Check to ensure the pump isn’t leaking ____

- Check to ensure that the pump is properly wired ____

#### Refrigerant Lines

- Check to ensure the refrigerant lines aren’t leaking ____

- Check to ensure the refrigerant lines aren’t damaged ____

- Check to ensure the refrigerant lines are insulated ____

- Check to ensure the refrigerant lines aren’t too warm or too cold ____

- Check to ensure the refrigerant lines aren’t touching each other ____

- Check the refrigerant lines for low points or improper slope ____

#### Thermostats

- Check to ensure that the thermostat is operational ____

- Check to ensure the thermostat is in an appropriate location ____

- Check to ensure the thermostat is level ____

- Check to ensure the thermostat isn’t loose ____

- Check to ensure the thermostat isn’t dirty ____

- Check to ensure the thermostat isn’t damaged ____

- Check to ensure the thermostat is properly adjusted/calibrated ____

#### Back-up Heat

- Check to ensure there’s a back-up heat method ____

- Check to ensure the back-up heat system is operational ____

- Check to ensure the system is properly located within the system ____

- Check to ensure that the system isn’t running continuously ____